## Slide 1: MCPS Systemwide Safety Programs Department of Facilities Management
Chemical Inventory, Safety Overview
Science Resource Teachers
July 6, 2016

## Slide 2: Systemwide Safety Programs Contacts
Peter Park, Team Leader
Peter_Park@mcpsmd.org
Laurie Lyons, Program Technician
Laurie_E_Lyons@mcpsmd.org
Office: 240-314-1070
Emergencies: 301-370-2141
www.montgomeryschoolsmd.org/departments/facilities/safety/
twitter.com/MCPSSafety

## Slide 3: Systemwide Safety Programs Mission
Help establish and maintain a safe, healthful learning and working environment for students, staff, contractors, and visitors.

## Slide 4: Systemwide Safety Programs Major Functions
Guidance/direction to facilities, offices, departments
Oversight of student and employee safety programs
Compliance with safety and health regulations
Coordinate safety training
Hazard evaluation, accident investigation

## Slide 5: Systemwide Safety Programs About Us
We are experts in the practice of safety/health
  identifying, anticipating, evaluating hazards
  determining feasible methods for controlling hazards
We are not experts on what you do (>520 MCPS job titles)
  we are not welders, teachers, principals, HVAC mechanics, bus drivers, building service workers, physical therapists, etc.
We must work with you to ensure effective, feasible safety/health procedures and control methods
We are busy, not rude (usually)

## Slide 6: Hierarchy of Hazard Controls
A concept used to protect workers from job hazards:
Ranks control method categories by effectiveness
Promoted/required by OSHA/MOSH

## Slide 7: Hierarchy of Controls
In order, by decreasing effectiveness:
Elimination/Substitution
Engineering Controls
  Lab hood, exhaust ventilation, safety shield
Administrative Controls/Work Practices
  Training, written procedures, housekeeping
Personal Protective Equipment (PPE)
  Gloves, goggles, apron, lab coat

## Slide 8: Hierarchy of Controls Why is PPE a last resort (least effective)?
Requires ongoing proper training
Must be properly selected
Must fit correctly
Must be used correctly
Must be used
Must be maintained, cleaned
Can be uncomfortable
Can create other hazards
  heat stress, impaired vision/dexterity/hearing/mobility
Use only when more effective controls are not feasible or 100% effective

## Slide 9: Hierarchy of Controls PPE – Proper Training, Use

## Slide 10: Hazardous Chemicals

## Slide 11: Hazardous Chemicals

## Slide 12: Hazardous Chemicals

## Slide 13: Hazardous Chemicals

## Slide 14: Hazardous Chemicals

## Slide 15: Hazardous Chemicals

## Slide 16: Hazardous Chemicals

## Slide 17: Hazardous Chemicals

## Slide 18: Hazardous Chemicals

## Slide 19: Hazardous Chemicals OSHA/MOSH Requirements
Maryland Occupational Safety and Health (MOSH)
Hazard Communication Standard, 29 CFR 1910.1200,
Laboratory Standard, 29 CFR 1910.1450
Complete inventory of hazardous chemicals – Chemical Information List (CIL)
Safety Data Sheet (SDS) for each hazardous chemical
Written Chemical Hygiene Plan (CHP)
Employee training, information, access to CILs and SDSs
Ensure containers labeled, label secondary containers
Maintain each CIL for at least 40 years, most SDSs/MSDSs for at least 30 years
Add new chemicals to CIL within 30 days

## Slide 20: Hazardous Chemicals County Requirements
Montgomery County Office of Emergency Management and Homeland Security (OEMHS)
Obtain hazardous materials use permit annually for all facilities
Maintain an alphabetical CIL
Include container types, sizes, amounts on CIL

## Slide 21: Hazardous Chemicals Pictograms – see handout
Chemical Type | Pictogram | Description | Examples
Explosives |  | Chemicals susceptible (by heat, shock, friction or other impulse) to a rapid chemical reaction, decomposition or combustion with the rapid generation of heat and gases. | organic peroxides; nitrogen triiodide; picric acid; potassium metal
Flammables |  | Chemicals with the potential to catch fire. Liquids, gases, solids (in the form of dusts) can be flammable and/or explosive. | propane; paint thinner; mastics; solvents (acetone, alcohols, acetic acid, hexane); adhesives (some)
Oxidizers/ Reactives |  | Chemicals that react violently when combined with heat, light water, or atmospheric oxygen, causing explosions or violent chemical reactions. | nitrates; chlorates; nitrites; peroxides; picric acid (crystallized); ethyl ether (crystallized); water reactive metals (e.g., sodium)
Compressed Gases |  | Gases stored under pressure such that cracks or damage to the tanks and valves could cause significant physical harm to those in the same room. | acetylene; helium; nitrogen

## Slide 22: Hazardous Chemicals Pictograms
Chemical Type | Pictogram | Description | Examples
Acute Toxics (Severe) |  | Any substance that, even in small amounts, can injure living tissue when ingested, inhaled, or absorbed. | mercury; arsenic; cyanide; mercuric chloride; sodium peroxide
Corrosives |  | Chemicals that can burn, irritate or destroy living tissue or corrode metal through direct chemical action. Includes strong acids and bases (alkaline) and dehydrating agents and oxidants. | sulfuric, nitric, hydrofluoric, and hydrochloric acids; potassium, ammonium, and sodium hydroxides (bases); hydrogen peroxide or chlorine (oxidants)
Chronic Health Hazards |  | Any substance that can cause chronic health effects. Includes carcinogens, mutagens, sensitizers, reproductive toxicants, target organ toxicants. | mercury; arsenic; lead; benzene; cadmium; chromium; PCBs; asbestos; wood dust
Acute Toxics |  | Substances that can cause acute health effects, such as irritation (eye, skin, respiratory), narcotic effects, sensitization. | refrigerants; isocyanates; acetic acid; ammonia; bromine

## Slide 23: Labels OSHA/MOSH Requirements
Name of chemical(s)
Hazards (physical and health) – can use pictograms
Manufacturer
Signal Word – Danger, Warning
Precautions

## Slide 24: Labels Label Pictograms?

## Slide 25: Chemical Information List (CIL) How do you inventory your lab chemicals?
Chemical Inventory Job Hazard Analysis (JHA)
Handout
Download at: http://www.montgomeryschoolsmd.org/uploadedFiles/departments/facilities/safety/JHAScienceChemicalInventory063016FINAL.pdf

## Slide 26: PPE – Glove Selection
Nitrile and neoprene or butyl should be sufficient
No glove can protect against all chemicals
Ensure proper fit, use, training
Do not immerse gloved hands in chemicals – gloves are not indestructible
Minimize contact with chemicals
Always wash hands after removing gloves

## Slide 27: PPE – Glove Selection
No latex, no vinyl medical or food service gloves

## Slide 28: PPE - Glove Selection Which material will protect you?
Check for information from:
Safety Data Sheet (SDS)
Chemical-resistant glove selection guides (Flinn - handout)
Glove manufacturer guides
  Ansell online guide http://www.ansellpro.com/specware/guide.asp
  Ansell downloadable guide www.ansellpro.com/download/Ansell_8thEditionChemicalResistanceGuide.pdf
  Showa Best online guide http://www.showagroup.com/innovation/chemical-resistance

## Slide 29: Glove Selection
Ansell Guide: http://www.ansellpro.com/download/Ansell_8thEditionChemicalResistanceGuide.pdf

## Slide 30: Hazardous Chemicals What if you have a large chemical (or any mercury) spill?
Evacuate, isolate the room or immediate area
Call 911 if severe, or immediate help needed
Provide first aid, as needed
Open windows and turn off HVAC, if feasible
Contact SSP (240-314-1070; 301-370-2141) or ES/IAQ (301-926-4409) immediately
Sequester potentially contaminated materials and occupants in nearby hall or room, if possible
Implement Shelter In Place, if needed
Do not attempt to clean the spill

## Slide 31: Online Safety Training
Mandatory online safety training for secondary science staff:
Bloodborne Pathogen Exposure Prevention – Annually
Science Lab Safety – Annually
Hazard Communication: Right to Understand
Safety Data Sheets: Globally Harmonized System (GHS)
New Process (no more PDO registration, PDO transcript):*
Go to SafeSchools at mcps.md.safeschools.com/login
Log on using your Outlook user name; no password is needed
The training home page will list mandatory and suggested (voluntary) training courses
Click any course name to begin training
Print a certificate of completion after completing each course
* Directions to take courses, view course completion records, and print/save certificates: http://www.montgomeryschoolsmd.org/departments/facilities/safety/training.aspx

## Slide 32: Systemwide Safety Programs Science Safety Page – SSP Website
www.montgomeryschoolsmd.org/departments/facilities/safety/health-guidance.aspx

## Slide 33: Questions?